## Slide 7: DC Motor

## Slide 8: Introduction
An electric motor is a machine which converts electric energy to mechanical energy.
If a current-carrying conductor is placed in a magnetic field produced by permanent magnets, then the field due to the current- carrying conductor and the permanent magnets interact and cause a force to be exerted on the conductor
The force on the current-carrying conductor in a magnetic field depends upon:
The flux density of the field B (teslas).
The strength of the current, I (Amperes).
The length of the conductor perpendicular to the magnetic field, l (meters).
The direction of the field and current (angle).

## Slide 11: Significance of the Back e.m.f.
When the motor armature rotates, the conductors also rotate and hence cut the flux. In accordance with the laws of electromagnetic induction, e,m.f. is induced in them whose direction, as found by Fleming's Right-hand Rule, is in opposition to supplied voltage. Because of its opposing direction, it is referred to as counter e.m.f. or back e.m.f. (ERbR).